## Slide 1: Phantom Powered Balanced Piezoelectric Contact Microphone
Designed and built by Anand Lobo

## Slide 2: Types of Microphone
Dynamic (unpowered, basically a speaker in reverse)
Condenser (uses an “electret”, requires power for circuitry)
  Condenser mics can have a battery or use “phantom power”

## Slide 3: Balanced Vs Unbalanced audio
Unbalanced: requires 1 signal + GND wire, most common
- any noise that affects the signal cannot be removed
Balanced: also known as “differential signal”, requires 2 signal wires
- rejects noise and (when properly implemented) boosts signal

## Slide 4: Phantom power
Most commonly 48V
Only usable with balanced signal wires
Avoid batteries
48V allows larger headroom (loudness before distortion)

## Slide 5: My microphone design
Three parts:
Balanced piezoelectric disc (the actual “pickup” transducer)
  the transducer alone can be used when phantom power is not available
  however, without the preamplifier it will sound similar to cheap piezoelectric pickups
TRS-XLR cable required (normal guitar cable will not work with preamp)
Phantom-powered preamplifier
Specifically called a “microphone” to avoid association with commercially available instrument pickups

## Slide 6: The pickup
Clamp and mount for violin / viola
Model for “general” instrument use

## Slide 7: The TRS-XLR cable
90-degree connector for violin/viola
Straight connector for other instruments

## Slide 8: The Preamplifier

## Slide 14: Main competition
AKG C-411: INR 10,000 - 20,000
  actually a miniature condenser microphone
  mounting solution known to leave blemishes/marks
Fishman V-200: INR 15,000 – 25,000
  mounts to bridge and can affect timbre
  additional preamplifier required for best sound quality
LR Baggs / Barcus Berry / similar
cheap piezo mics available online and in stores (no preamp and no instruction)
normal vocal / instrument microphones
  Shure
  Sennheiser
  Neumann
  AKG

## Slide 15: Use Cases
Can be used on any hollow-body resonating instrument
  successfully tested with violin-family, guitar-family, piano, kalimba (see website)
Indian instruments
Nature recording
ASMR
Seismometer (?)
Industrial monitoring (?)
Hydrophone (with suitable waterproofing)
Throat microphone / body monitoring e.g. heartbeat

## Slide 16
Preliminary recordings:
https://ohnoitsalobo.github.io/pickup